| West Virginia Department of Environmental Protection |
| --- |
| Joe Manchin, III Governor | Division of Air Quality | Randy C. Huffman Cabinet Secretary |

Application Instructions and Forms for General Permit G50-B

for the

Prevention and Control of Air Pollution in regard to the

Construction, Modification, Relocation, Administrative Update and

Operation of Concrete Batch Plants

THIS REFERENCE DOCUMENT PROVIDES DEFINITIONS, INFORMATION, FORMS AND INSTRUCTIONS TO BE USED WHEN PREPARING A REGISTRATION APPLICATION FOR CLASS II GENERAL PERMIT NUMBER G50-B. THE INFORMATION PROVIDED IN THIS DOCUMENT ADDRESSES THE REQUIRED COMPONENTS OF AN ADMINISTRATIVELY COMPLETE REGISTRATION APPLICATION.

Revised:  March 18, 2009

Table of Contents

1.0.	Definitions	3

2.0.	Class II General Permit Registration Application Requirements	7

Example Legal Advertisement	11

Siting Criteria Waiver	13

3.0. Control Device Identification Number Instructions	14

Table A – Control Device Listing	15

G50-B Registration Forms	16

CBP Production Affected Source Sheet	17

Air Pollution Control Device Affected Source Sheet	18

CBP Particulate Matter Capture System Affected Source Sheet	19

CBP Material Storage & Handling Affected Source Sheet	20

CBP Fugitive Dust Control System Affected Source Sheet	21

CBP Storage Tank Affected Source Sheet	22

CBP Emission Summary Sheets	23

General Permit Permit Levels	24

- Definitions

Terms used throughout the General Permit are defined in this section. Unless otherwise indicated, other words and phrases used in this General Permit shall have the meaning ascribed to them in 45CSR7, 45CSR13, 45CSR22; W.Va. Code §§22-5-1 et seq., as amended.

AIR POLLUTANT

means any solid, liquid or gas which if discharged into the air, may result in statutory air pollution.

AIR POLLUTION OR STATUTORY AIR POLLUTION

means and is limited to the discharge into the air by an act of man substances (liquid, solid, gaseous, organic or inorganic) in a locality, manner and amount as to be injurious to human health or welfare, animal or plant life or property, or which would interfere with the enjoyment of life or property.

AIR POLLUTION CONTROL DEVICE or APCD

means any equipment, auxiliary air pollution control device, system or element of design which controls or reduces the emission of substances from an emissions unit or stationary source:

- Primary Collection means that air pollution control device such as cyclones or multicyclones incorporated for the collection of fine particulate matter generated and emitted principally from the drying operation and from which all collected material may or may not be reinjected into the main aggregate flow; and

- Secondary Collection means that air pollution control device (e.g. bag filters or baghouse) incorporated for the collection of that particulate matter not collected by the primary collection equipment and from which such collected material may or may not be reinjected into the main aggregate flow. A secondary collection air pollution control device may incorporate a settling or knockdown chamber which performs the function of a primary collection device.

AUTHORIZED REPRESENTATIVE

means a person certified by a Responsible Official who shall represent and have the authority to legally bind the business. An Authorized Representative may be certified through a certification statement submitted with the General Permit Registration Application. Such certification is subject to approval by the Director.

AUXILIARY AIR POLLUTION CONTROL DEVICE

means any device or element of design that senses temperature, pressure drop or any other parameter for the purpose of activating, controlling, modulating, delaying or deactivating the operation of any part of air pollution control device.

CABINET SECRETARY

means the Cabinet Secretary of the West Virginia Department of Environmental Protection.

C.F.R.

means the United States Code of Federal Regulations.

CSR

means the West Virginia Code of State Rules.

CONSTRUCTION

means any physical change or change in the method of operation (including fabrication, erection, installation, demolition or modification of an emissions unit or affected facility) which would result in an increase in the potential to emit or an increase in actual emissions of any regulated air pollutant.

DAQ

means the Division of Air Quality of the WV Department of Environmental Protection.

DEP

means the Department of Environmental Protection of the West Virginia Bureau of the Environment.

DIRECTOR OF AIR QUALITY OR DIRECTOR

means the Director of the Division of Air Quality or a designated representative appointed by the Cabinet Secretary of the Department of Environmental Protection pursuant to the provisions of W.Va. Code §§22-1-1 et seq.

EMISSION

means the release, escape or discharge of air pollutants into the air.

EMISSION INVENTORY

means an annual submittal, due on or before July 1 of each calendar year for the previous calendar year, containing the speciated pollutants and the corresponding emission poundage or tonnage for each (W.Va. Code §22-5-4(a)(14)).

EMISSIONS UNIT

means any affected facility, part or activity of a stationary source which emits or has the potential to emit any regulated pollutant.

EPA OR USEPA

means the United States Environmental Protection Agency.

FUGITIVE EMISSIONS

means those emissions which could not reasonably pass through a stack, chimney, vent or other functionally equivalent opening.

FUGITIVE PARTICULATE MATTER

means any and all particulate matter generated by the operation of a concrete batch plant which, if not confined, would be emitted directly to the atmosphere from points other than the stack outlet.

FUGITIVE PARTICULATE MATTER CONTROL SYSTEM

means, for purposes of this General Permit, any equipment or method used to confine, collect and dispose of fugitive particulate matter, including but not limited to: hoods, bins, ductwork, fans, air pollution control equipment and equipment used to prevent or minimize the emission of fugitive particulate matter by application of water or a mixture of water and an environmentally acceptable dust control additive (solution).

MAINTENANCE OPERATION

means any adjustment, repair, removal, disassembly, cleaning or replacement of components or systems of emission units or air pollution control devices required to be performed on a periodic basis to prevent part failure or malfunction, or those actions anticipated as necessary to correct an overt indication of malfunction or failure for which maintenance is not appropriate.

MAJOR STATIONARY SOURCE OR MAJOR SOURCE

means, for purposes of this General Permit, any stationary source which emits or has the potential to emit two hundred fifty (250) tons per year or more of any regulated air pollutant as defined in 45CSR14 or directly emits or has the potential to emit one hundred (100) tons per year or more of any air pollutant as defined in 45CSR30.

MODIFICATION

means, for purposes of this General Permit, any proposed physical change or change in the method of operation of an affected facility that would require an individual permit pursuant to 45CSR13.  Any person operating an existing affected facility who desires to modify and/or increase throughput may complete a General Permit Registration Application and if eligible, receive General Permit registration in lieu of individual permit coverage pursuant to 45CSR13.

OPACITY

means the degree to which particulate emissions reduce the transmission of light and obscure the view of an object in the background.

PARTICULATE MATTER OR PM

means any material except uncombined water that exists in a finely divided form as a liquid or solid.

PARTICULATE MATTER CAPTURE SYSTEM

means any equipment or method used to confine, collect, and transport particulate matter from elevators, screens, mixers, weighing equipment, bins and other plant components to air pollution control equipment. Particulate matter capture systems shall include, but not be limited to, hoods, bins, ductwork, enclosures and fans.

PM10

means any particulate matter with an aerodynamic diameter less than or equal to a nominal 10 micrometers.

PERSON

means any and all persons, natural or artificial, including the State of West Virginia or any other state, the United States of America, any municipal, statutory, public or private corporation organized or existing under the laws of this or any other state or country and any firm, partnership or association of whatever nature.

PLANT OR CONCRETE BATCH PLANT

means and includes, for purposes of this General Permit, all the equipment utilized in the manufacture of truck-mixed or central-mixed Portland cement concrete (ready mix), concrete block, concrete brick and/or grout typically comprised as a combination of the following: systems for loading, transferring and storing sand, aggregate, cement, admixtures and additives such as feed hoppers, conveyors, stockpiles, front-end loaders, elevators, pneumatic transfer systems, permanent or portable storage structure and silos; production weigh hoppers, water delivery systems, dispenser systems, central mixers; storage tanks, particulate matter capture systems, air pollution control devices and fugitive dust control systems; paved and unpaved haulroads; work, casting, storage and parking areas.

POTENTIAL TO EMIT

means the maximum capacity of an affected facility to emit any pollutant under its existing or proposed physical and operational design.

REGISTRANT

means a person who has submitted a General Permit Registration Application and has been granted General Permit registration by the Director.

REGISTRATION

means the process where the owner or operator of an eligible affected facility submits a complete General Permit Registration Application and is granted General Permit registration.

REGISTRATION MODIFICATION

means the General Permit provision for any proposed physical change or change in the method of operation of a registered affected facility.

RELOCATION

means the physical movement of a source outside its existing plant boundaries.

RESPONSIBLE OFFICIAL

means a person who shall represent the business and is a President, Vice President, Secretary, Treasurer, General Partner, General Manager, a member of a Board of Directors or Owner, depending on business structure. Any submitted Registration Application, report, Emission Inventory, Certified Emission Statement, compliance certification record or Certification of Data Accuracy shall be signed by a Responsible Official or an Authorized Representative. A Responsible Official or an Authorized Representative shall have the authority to legally bind the business. An Authorized Representative may be certified by a Responsible Official through a certification statement submitted with the General Permit Registration Application. Such certification is subject to approval by the Director.

SMOKE

means any small gasborne and airborne particles arising from a process of combustion in sufficient numbers to be visible.

SOURCE OR STATIONARY SOURCE

means, for purposes of this General Permit, any building, structure, affected facility, installation or emission unit or combination thereof which emits or may emit any regulated air pollutant.

STACK

means, but shall not be limited to, any duct, control equipment exhaust or similar apparatus which vents gases containing any regulated pollutant into the open air.

STANDARD CONDITIONS

means, for purposes of this General Permit, a temperature of 68oF (20o C) and a pressure of 29.92 inches of mercury (760 mm of Hg).

2.0.  Class II General Permit Registration Application Requirements

The Registration Application requires the following information.  Failure to submit this information may result in the Registration Application being deemed incomplete.

Section I.  General Information

Complete Section 1 of the Application for General Permit Registration.  Use the following guidelines to ensure a complete application:

1.	Name of Applicant as registered with the WV Secretary of State’s Office.

2.	Federal Employer ID Number (FEIN)

3.	Applicant’s Mailing Address

4.	If applicant is a subsidiary company please provide the name of the parent company

5.	Provide as Attachment A a copy of the current WV Business Registration.

Section II. Facility Information

Complete Section 2 of the Application for General Permit Registration.  Use the following guidelines to ensure a complete application:

7.	Type of Plant or Facility (Concrete Batch Plant)

8.	Standard Industrial Classification (SIC) Code for the Affected facility (3271, 3273)

9.	Division of Air Quality Facility ID Number (for existing affected facilities).  ID# _ _ _ - _ _ _ _ _

10.	List all current DAQ permit numbers associated with this affected facility, include any Rule 13 and Title V permits.

Operating Site Information

Complete Section 3 of the Application for General Permit Registration.  Use the following guidelines to ensure a complete application:

11.	Name of Primary Operating Site

12.	Operating Site’s Mailing Address

13.  Does the Applicant own, lease, have an option to buy, or otherwise have control of the proposed site?

Yes – Please Explain.  No – You are not eligible for a permit for this source.

14.	Directions to Operating Site

15.	Nearest City or Town

16.  County

17.	UTM Northing (km)

18.  UTM Easting (km)

19.  UTM Zone

The Universal Transverse Mercator (UTM) coordinate system is a grid-based method of specifying locations on the surface of the Earth. It is used to identify locations on the earth, but differs from the traditional method of latitude and longitude in several respects.  The UTM system is not a single map projection. The system instead employs a series of sixty zones, each of which is based on a specifically defined secant Transverse Mercator projection.  However, if you know your latitude and longitude our website offers the capability of converting these to UTM coordinates.

20.	Anticipated installation or change date

21.	Anticipated startup date

22.	Operating Schedule including hours of operation per day, days of operation per week, and weeks of operation per year.

Section III.  Attachments and Supporting Documents

Attachment A - Current Business Certificate

If the registrant is a resident of the State of West Virginia the registrant should provide a copy of the registrant’s current Business Registration Certificate issued to them from the West Virginia State Tax Department.  If the registrant is not a resident of the State of West Virginia, the registrant should provide a copy of the Certificate of Authority/Authority of LLC/Registration.

Attachment B - Process Description

Provide a detailed written description of the operation, plant and/or affected facilities. The Process Description is used in conjunction with the Process Flow Diagram to provide the reviewing engineer a complete understanding of the activity at the operation or plant. Describe in detail and order the complete process.

Use the following guidelines to ensure a complete Process Description:

1.	The Process Flow Diagram should be prepared first and used as a guide when preparing the Process Description. The written description shall follow the logical order of the Process Flow Diagram.

2.	All sources, affected facilities, and air pollution control devices must be included in the Process Description.

3.	When modifications are proposed, describe the modifications and the effect the changes will have on affected facilities, equipment or operation.

4.	Proper Source Identification Numbers are used consistently in the Process Description.

5.	Additional information that may facilitate the reviewer's understanding of the Process Flow Diagram and/or Process Description is included.

Attachment C – Description of Fugitive Emissions

Provide a detailed written description of all potential sources of fugitive particulate emissions such as stockpiles, haulroads, and vehicle traffic from work areas.  Describe methods and fugitive dust control equipment which will be utilized for each potential source of fugitive emissions.  The description of fugitive emissions shall also outline fugitive dust control measures or best management practices to be employed on haulroads, stockpiles, and work areas.  Use the following guidelines to ensure a complete Description of Fugitive Emissions:

- Describe all sources and potential sources of fugitive particulate emissions.

- Describe all fugitive dust control equipment.

- Provide the application rate of water, or if using solution, mix ratio and type used at sprays.

- Provide the application frequency of water or solution to haulroads and work areas during dry periods.

- Describe methods employed to winterize sprays.

- Indicate type of haulroad surface(s) that will be maintained such as asphalt pavement, concrete, dirt, coarse gravel, etc.

- Describe fugitive dust control methods and related equipment for any highwall truck or conveyor dump.

- Describe any other method or practice implemented to minimize fugitive particulate emissions.

Attachment D – Process Flow Diagram

Provide a diagram or schematic that supplements the Process Description of the operation or plant. The Process Flow Diagram shall show all sources, components or facets of the operation or plant in an understandable line sequence of operation. Appropriate sizing and specifications of equipment should also be shown on the Process Flow Diagram. For a proposed modification, clearly identify the process areas, affected facilities and equipment that will be modified or added, and specify the nature and extent of the modification.

Use the following guidelines to ensure a complete Process Flow Diagram:

1.	The Process Flow Diagram shall logically follow the entire process from beginning to end.

2.	Identify each source, air pollution control device and transfer point with proper and consistent Source Identification Numbers, Control Device Identification Numbers and Transfer Point Identification Numbers.

3.	Include material handling rates for all lines of the Process Flow Diagram. If applicable, include pre- and post-modification material handling rates and identify accordingly.

4.	Transfer Point Identification Numbers, consistent with assignments in any emission calculation sheet, should be shown at each transfer point.

5.	The process flow lines may appear different for clarity. For example, dot-dash-dot for raw material, and a solid line for finished product. Refuse flow may be identified by a dotted line

6.	The process flow lines may be color coded. For example, new or modified equipment may be red, old or existing equipment may be blue; different stages of preparation such as raw material may be green and finished product or refuse another color.

Attachment E – Plot Plan

Provide an accurately scaled and detailed Plot Plan showing the locations of all process equipment and/or affected facilities and air pollution control devices. Show all equipment, affected facilities, enclosures, buildings and plant entrances and exits from the nearest public road(s) as appropriate. Note height, width and length of proposed or existing buildings and structures.

A scale between 1"=10' and 1"=200' should be used with the determining factor being the level of detail necessary to show operation or plant areas, affected facilities, sources, transfer points, etc. An overall small scale plot plan (e.g., 1"=300') should be submitted in addition to larger scale plot plans for process or activity areas (e.g., 1"=50') if the plant is too large to allow adequate detail on a single plot plan. Process or activity areas may be grouped for the enlargements as long as sufficient detail is shown.

Use the following guidelines to ensure a complete Plot Plan:

1.	Operation, plant or facility name

2.	Company name

3.	Company ID number

4.	Plot scale, north arrow, date drawn, and submittal date.

5.	Fence lines

6.	Property lines

7.	Base elevation

8.	UTM reference coordinates from the Area Map and corresponding reference point elevation

9.	Location of all sources labeled with proper and consistent Source Identification numbers

This information is required for all sources regardless of whether it is a construction, modification, or administrative update.

Attachment F – Area Map

Provide a USGS 7.5 minute topographic Area Map showing the current or proposed location of the operation or plant.  On this map, identify plant or operation property lines, access roads and any adjacent dwelling, business, public building, school, church, cemetery, community or institutional building or public park.

Mark and reference UTM coordinates (not latitude and longitude) and the corresponding elevation above mean sea level for the operation or plant. UTM coordinates may be acquired from the USGS 7.5" topographical map. UTM coordinates are marked as blue tick marks along the outside edges of the map. These coordinates must be provided for a point inside the plant boundary near the center of the property and be accurate to within fifty meters.

This information is required for all sources regardless of whether it is a construction, modification, or administrative update.

Attachment G – Affected Source Sheets (Section Applicability Form)

Provide the appropriate Equipment Data Sheets and Affected Source Sheets (CBP Production Equipment, Air Pollution Control Device, Particulate Matter Capture System, Material Storage and Handling, Fugitive Dust Control System, CBP Storage Tank, and Pollutant Summary Sheets). These forms can be found beginning on page 16.  Proper Source Identification Numbers must be used consistently throughout the Registration Application.  Refer to Table A – Control Device Listing for guidance on assigning control device identification numbers.  Proper source and control device identification numbers must be used consistently throughout the Registration Application.  Transfer point identification number shall be assigned to transfer points in the Emission Calculation Sheet.

Use the following guidelines to ensure complete Affected Source Sheets:

1.	Proper Control Device Identification Numbers are assigned to all emission control devices.

2.	Proper Source Identification Numbers are assigned to all crushing and screening equipment, transfer and conveying equipment, stockpiles and storage areas.

Attachment H - Air Pollution Control Device Data Sheet

If air pollution control devices are utilized (baghouse), complete and attach to the Class II General Permit Registration Application the applicable Air Pollution Control Device Sheet for each unit.

Attachment I - Emissions Calculations

Provide detailed emission calculations which lists the plant or operation’s potential to emit (PTE) for criteria and hazardous/toxic pollutants.

Use the following guidelines to ensure complete emission calculations

1.	All emission sources (including transfer points) are included in the emission calculations, as well as all methods used in the emissions calculations.

2.	Proper Source Identification Numbers and Control Device Identification Numbers are used consistently in the Emission Calculations.

3.	A printout of the Emission Summary Sheets is attached to the Registration Application.

4.	A printout of the Input Form is attached to the Registration Application.

Attachment J – Class I Legal Advertisement

Publication of a proper Class I legal advertisement is a requirement of the application process.  In the event the applicant’s legal advertisement fails to follow the requirements of 45CSR 13 (45-13-8) or the requirements of Chapter 59, Article 3, of the West Virginia Code, the application will be considered incomplete.

The applicant, utilizing the format for the Class I legal advertisement appearing below, shall cause such legal advertisement to appear a minimum of one (1) day in the newspaper most commonly read in the area where the affected facility exists or will be constructed.  The notice must be published no earlier than five (5) working days of receipt by this office of your application.  If this happens, the applicant may be required to republish the notice.  The original affidavit of publication must be received by this office no later than the last day of the public comment period.

The advertisement shall contain, at a minimum, the name of the applicant, the type and location of the source, the type and amount of air pollutants that will be discharged, the nature of the permit being sought, the proposed start-up date for the source and a contact telephone number for more information.

The location of the source should be as specific as possible starting with:   1.) the street address of the source (If no street address is available, provide location relative to the closest intersection or mile marker); 2.) the nearest street or road; 3.) the nearest town or unincorporated area, and 4.) the county.

If the location description is not sufficiently detailed, the DAQ may require the applicant to republish the Class I legal advertisement.

Types and amounts of pollutants discharged must include all regulated pollutants (PM, PM10, VOC, SO2, NOx, formaldehyde, benzene, toluene, ethylbenzene, xylene, and n-hexane) and their potential to emit or the permit level being sought in units of tons per year.

In the event the 30th day is a Saturday, Sunday, or legal holiday, the comment period will be extended until 5:00 p.m. on the following regularly scheduled business day.

An example Class I legal advertisement is included below:

EXAMPLE LEGAL ADVERTISEMENT

AIR QUALITY PERMIT NOTICE

Notice of Application

Notice is given that (Applicant’s Legal Name) has applied to the West Virginia Department of Environmental Protection, Division of Air Quality, for a (General Permit Registration, Class II Administrative Update,) for a (Type of Operation) located on (Street Name, Road Number, etc.), (in/near City or Town), in (County Name) County, West Virginia.

The applicant estimates the (Increased, if modification application) potential to discharge the following Regulated Air Pollutants will be: (Pollutants and associated amounts in tons per year).

Startup of operation is planned to begin on or about the (Day) day of (Month), (Year).  Written comments will be received by the West Virginia Department of Environmental Protection, Division of Air Quality, 601 57th Street, SE, Charleston, WV  25304, for at least 30 calendar days from the date of publication of this notice.

Any questions regarding this permit application should be directed to the DAQ at (304) 926-0499, extension 1227, during normal business hours.

Dated this the (Day) day of (Month), (Year).

By:	(Applicant’s Legal Name)

(Name of Responsible Official)

(Title of Responsible Official)

(Mailing Address)

(City, State and Zip Code)

Attachment K - Electronic Submittal (Optional)

Provide an Electronic Submittal Diskette(s) for all files that are available electronically. The Electronic Submittal Diskette should have the following files in their respective formats (if available):

1.	Registration Application file (Microsoft Word or Word Perfect format)

2.	Affected Source Sheets (Microsoft Word or Word Perfect format)

3.	Process Flow Diagram file

4.	Process Description file (Microsoft Word or Word Perfect format)

5.	Area Map file

6.	Plot Plan file

7.	Emission Calculations Spreadsheet (Microsoft Excel format)

8.	Air Pollution Control Device Sheet, if required (Microsoft Word or Word Perfect format)

Section IV.  Certification of Information

Any General Permit Registration Application shall be signed and certified by a Responsible Official or Authorized Representative as set forth in the General Permit G50-B. Such signature shall constitute an agreement that the applicant will assume responsibility for the construction, modification, relocation, administrative update and/or operation of the stationary source in accordance with the Registration Application, the requirements, provisions, standards or conditions of the General Permit, any other permit or applicable statutory or regulatory requirement (45CSR13).  Certify whether or not the registrant is a Corporation, Partnership, Limited Liability Company, Association, Joint Venture, or a Sole Proprietorship.

If the General Permit Registration Application is not signed, it will be returned to the applicant.

Attachment L - General Permit Registration Application Fee

A person submitting a Class II General Permit Registration Application to construct, modify, relocate or administratively update a coal preparation plant and/or coal handling operation shall pay a Class II General Permit registration fee pursuant to 45CSR13.  The registration fee shall be paid by a negotiable instrument (check, draft, warrant or money order) to DEP - Division of Air Quality. The fees associated with General Permit G50-B include:

1.	$500.00 for Class II General Permit Registrations (Construction/Modification)

2.	$300.00 for Class II administrative updates

Any submitted Registration Application shall not be deemed to have been received nor administratively complete unless payment of the proper Class II General Permit registration fee(s) is (are) included (45CSR22);

Any General Permit registration fee paid hereunder is not refundable (45CSR22).

Attachment M - Siting Criteria Waiver

If registrant is seeking a waiver from the siting criteria in G50-B, please complete the siting criteria waiver.  This waiver needs to be completed by the registrant and person(s) granting the waiver, and notarized by an authorized West Virginia Notary Public.  The waiver is only good for the submitted registration application.  Therefore, any further modification or administrative update requiring public notice will require a new waiver.

Siting Criteria Waiver

Division of Air Quality 300’ Waiver

I ________________________________________________ hereby

Print Name

acknowledge and agree that _______________________________________ will

General Permit Applicant’s Name

construct a concrete batch plant

that will be located within 300’ of my dwelling.

I hereby offer this waiver of siting criteria to the West Virginia Department of Environmental Protection Division of Air Quality as permission to construct, install and operate in such location.

Signed:

______________________________________________________________

Signature    Date

______________________________________________________________

Signature    Date

# Taken, subscribed and sworn before me this _____ day of

_______________________, 20_____.

My commission expires:  ________________________

SEAL__________________________________________________

Notary Public

- Control Device Identification Number Instructions

For sources which use an emission control device, appropriate control efficiency corrections must be made. Where control efficiencies are known from source tests or control equipment vendor guarantee, such efficiency should be used. Otherwise the values for the control efficiency of various control methods are listed in Table A of this Reference Document. For clarity, the identification of control systems should adhere to the following nomenclature:

For consistency, all Control Devices referenced in the Registration Application should appear in the following Control Device Identification Number format:

XX - YY#

Where:		XX = two letter abbreviation indicating the type of operation

YY = two letter abbreviation indicating the type of control device

# = number assigned to specific operation/device combination starting with 1,2,3

Combinations of these abbreviations for specific types of operations and corresponding control alternatives appear in Table A. These operation/device combinations should be used.

NOTE: If a single control device is used to control multiple operations, the abbreviation for the primary operation should be used for the Control Device Identification Number. Each individual control device should have only one Control Device Identification Number (refer to Example 2).

EXAMPLE 1:

A facility has a total of five pressurized spray bar water sprays employed to control fugitive emissions from open conveyor transfer points. From Table A - Control Device Listing, under the Transfer and Conveying section, water sprays at such transfer points are abbreviated as TC-WS. Therefore, in this example, the assigned Control Device Identification numbers for these five water sprays would be TC-WS1, TC-WS2, TC-WS3, TC-WS4 and TC-WS5. These Control Device Identification numbers should be used throughout the Registration Application to reference the respective water sprays.

EXAMPLE 2:

A facility’s water truck is primarily used for controlling haulroad emissions, but  also utilizes a fire hose type spray to wet open stockpiles to control wind erosion. In this case, a control device is used for multiple operations. From Table A for Haulroads, a water truck is abbreviated as HR-WS. However, stockpile watering to control wind erosion is abbreviated as SW-WS. In this case the water truck should be labeled as HR-WS1 for both haulroad control and stockpile wind erosion control since haulroads are the primary purpose. This single Control Device ID# should be used throughout the application when referencing the water truck.

TABLE A - CONTROL DEVICE LISTING

| Fugitive Dust Sources | Control Device* | Control Device Prefix | Control Efficiency (%) |
| --- | --- | --- | --- |
| UNLOADING |
| From Railcar or Truck | Full Enclosure Vented to Baghouse | UL-BH | 99 |
| From Railcar or Truck | Full Enclosure | UL-FE | 70 |
| From Railcar or Truck | Wet Suppression with Chemical Solution | UL-CS | 80 |
| From Railcar or Truck | Water Spray | UL-WS | 50 |
| Dump Bins | Full Enclosure | UD-FE | 80 |
| Dump Bins | Partial Enclosure with water sprays | UD-PW | 85 |
| CRUSHING AND SCREENING |
| Crushing or Screening | Full Enclosure Vented to Baghouse | CS-BH | 99 |
| Crushing or Screening | Wet Suppression with Chemicals | CS-CS | 90 |
| Crushing or Screening | Full Enclosure with Water Spray | CS-FW | 90 |
| Crushing or Screening | Partial Enclosure with Water Spray | CS-PW | 80 |
| Crushing or Screening | Full enclosure | CS-FE | 80 |
| TRANSFER AND CONVEYING |
| Conveyor Transfer Point | Full Enclosure Vented to Baghouse | TC-BH | 99 |
| Conveyor Transfer Point | Full Enclosure with Water Spray | TC-FW | 90 |
| Conveyor Transfer Point | Water Spray with Chemical Solution | TC-CS | 90 |
| Conveyor Transfer Point | Partial Enclosure with Water Spray | TC-PW | 80 |
| Conveyor Transfer Point | Full enclosure | TC-FE | 80 |
| Conveyor Transfer Point | Water spray | TC-WS | 70 |
| Conveyor Transfer Point | Partial Enclosure | TC-PE | 50 |
| CLEANING |
| Wet Wash Operations | Full Enclosure | WW-FE | 100 |
| STORAGE |
| Loading onto Piles | Full Enclosure | SL-FE | 80 |
| Loading onto Piles | Telescopic Chute | SL-TC | 75 |
| Loading onto Piles | Wet Suppression with Chemical Solution | SL-CS | 75 |
| Loading onto Piles | Wind Guard | SL-WG | 50 |
| Wind Erosion | Full Enclosure | SW-FE | 100 |
| Wind Erosion | Wet Suppression with Chemical Solution | SW-CS | 99 |
| Wind Erosion | Water Spray | SW-WS | 75 |
| LOADING OUT |
| From Stockpiles | Wet Suppression with Chemical Solution | LO-CS | 95 |
| From Stockpiles | Under-pile Conveyor | LO-UC | 80 |
| From Stockpiles | Bucket Wheel Reclaimer | LO-RC | 80 |
| LOADING |
| To Railcar, Barge or Truck | Wet Suppression with Chemical Solution | LR-CS | 80 |
| To Railcar, Barge or Truck | Telescopic Chute | LR-TC | 75 |
| HAULROADS |
| Unpaved | Water Truck with Chemical Solution | HR-CS | 85 |
| Unpaved | Water Truck with Water Spray | HR-WS | 70 |

* Refer to Control Device Identification Number Instructions

G50-B REGISTRATION

APPLICATION FORMS

# CBP PRODUCTION AFFECTED SOURCE SHEET

| CBP Production Information | Source Identification Number1 |  |  |
| --- | --- | --- | --- |
|  | Manufacturer & Model Number |  |  |
|  | Date of Manufacture |  |  |
|  | Maximum Design Production Rate2 |  |  |
|  | Maximum Annual Production3 |  |  |
|  | Daily Operation |  | hours/day |
|  | Annual Operation |  | days/year |
|  |  |  | hours/year |
|  | Approximate Percentage of Operation from: |  | Jan - Mar |
|  |  |  | April - June |
|  |  |  | July - Sept |
|  |  |  | Oct - Dec |

- Enter the appropriate Source Identification Number for each concrete batch plant production weigh hopper or central mixer. Batch plant weigh hopper should be designated WH-1, WH-2, etc. Batch plant central mixer should be designated CM-1, CM-2, etc.

- Enter the manufacturer’s Maximum Design Production Rate of the concrete batch plant production equipment. Specify units in tons/hour.

- Enter the Maximum Annual Production of the concrete batch plant. Specify units of cubic yards per year or tons per year. To calculate Maximum Annual Production, multiply the Maximum Design Production Rate (tons/hr) by the Annual Operation (hrs/yr).

AIR POLLUTION CONTROL DEVICE AFFECTED SOURCE SHEET

| CBP Air Pollution Control Device Data Sheet | Fabric Filter Baghouse | Filter Vent | Fabric Filter Discharge Sock |
| --- | --- | --- | --- |
| General Information | APCD Identification Number1 |  |  |  |
|  | Manufacturer & Model Number |  |  |  |
|  | Number of Compartments |  |  |  |
|  | Gas Inlet Area (ft2) |  |  |  |
|  | Gas Outlet Area (ft2) |  |  |  |
|  | Fabric Filter Cleaning Mechanism2 |  |  |  |
|  | Total Cloth (fabric) Area (ft2) |  |  |  |
|  | Draft Fan HP |  |  |  |
|  | Outlet Stack Area (ft2) |  |  |  |
| Operational Parameters | Minimum Design PD (in H2O) |  |  |  |
|  | Maximum Design PD (in H2O) |  |  |  |
|  | Inlet Gas Flow Rate (ACFM) |  |  |  |
|  | Inlet Gas Temperature (oF) |  |  |  |
|  | Inlet Gas Pressure (PSIA) |  |  |  |
|  | Inlet Gas Velocity (ft/sec) |  |  |  |
|  | PM Inlet Rate (grains/scf) |  |  |  |
|  | PM Outlet Rate (grains/scf) |  |  |  |
|  | Operating Air/Cloth Ratio (ft/min) |  |  |  |

1.  Enter the appropriate Air Pollution Control Device Identification Number for each fabric filter baghouse, filter vent or discharge sock. The devices should be designated APCD-1, APCD-2, APCD-3, etc.

2. Enter method used to clean bags: shaker, pulse jet, reverse jet or other.

3. Complete more than one CBP Air Pollution Control Device Data Sheet if necessary.

4. Enter the fractional efficiency of the fabric filter baghouse.

CBP PARTICULATE MATTER CAPTURE SYSTEM

AFFECTED SOURCE SHEET

Pursuant to Section 2.2.4 of General Permit G50-B, the registrant shall not cause, suffer, allow, or permit any registered concrete batch plant to operate that is not equipped with an effective particulate matter capture system(s) and associated air pollution control device(s) to minimize the emission of particulate matter from production equipment, storage structures and silos. The particulate matter capture system shall ensure the lowest fugitive particulate emissions reasonably achievable.

A particulate matter capture system shall be used to confine, collect, and transport displaced particulate matter from production weigh hoppers, cement and flyash storage structures and/or silos to an air pollution control device. Particulate matter capture systems may include but not be limited to: hoods, bins, ductwork, enclosures and air pollution control devices such as fabric filter baghouses, associated fans, discharge socks and filter vents.

Provide a written description of the concrete batch plant’s particulate matter capture system below:

CBP MATERIAL STORAGE & HANDLING

AFFECTED SOURCE SHEET

| Source Identification Number1 |  |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- |
| Material Stored2 |  |  |  |  |  |  |
| Maximum Yearly Throughput (tons/year)3 |  |  |  |  |  |  |
| Typical Moisture Content (%)4 |  |  |  |  |  |  |
| Average % of Material Passing Through 200 Mesh Sieve5 |  |  |  |  |  |  |
| Maximum Stockpile Base Area (ft2)6 |  |  |  |  |  |  |
| Maximum Stockpile Height (ft)7 |  |  |  |  |  |  |
| Maximum Storage Capacity (tons)8 |  |  |  |  |  |  |
| Dust Control Method Applied to Storage9 |  |  |  |  |  |  |
| Method of Material Load-in to Bin or Stockpile10 |  |  |  |  |  |  |
| Dust Control Method Applied During Load-in11 |  |  |  |  |  |  |
| Method of Material Load-out from Bin or Stockpile10 |  |  |  |  |  |  |
| Dust Control Method Applied During Load-out11 |  |  |  |  |  |  |
| 1. Enter the appropriate Source Identification Number for each storage activity using the following codes. For example, if the facility utilizes four open stockpiles and one storage silo, the Source Identification Numbers should be OS-1, OS-2, OS-3, and OS-4; and BS-1, respectively. OS Open Stockpile E3 Enclosure (three-sided enclosure) BS Bin or Storage Silo (full enclosure) SB Storage Building (full enclosure) SF Stockpiles with wind fences OT Other (please specify) 2. Describe the type of material stored or stockpiled. 3. Enter the maximum yearly storage throughput for each storage activity. 4. Enter the average percent moisture content of the stored material. 5. Enter the average percent of material that will pass through a 200 mesh sieve. 6. For stockpiles, enter the maximum stockpile base area. 7. For stockpiles, enter the maximum stockpile height. 8. Enter the maximum storage capacity for each storage activity in tons (e.g. silo capacity, maximum stockpile size, etc.). 9. Enter the dust control method applied to storage activity using the following codes: CA Crusting Agent WS Water Spray FE Full Enclosure NO None OT Other ___________________________ (please specify) 10. Enter the method of load-in or load-out to/from stockpiles or bins using the following codes: FE Front Endloader SS Stationary Conveyor/Stacker ST Stacking Tube MC Mobile Conveyor/Stacker CS Clamshell TD Truck Dump OT Other ___________________________ (please specify) 11. Enter the dust control method applied during load-in or load-out using the following codes: CA Crusting Agent WS Water Spray FE Full Enclosure MD Minimize Drop Height ST Stacking Tube NO None OT Other ___________________________ (please specify) |

CBP FUGITIVE DUST CONTROL SYSTEM

AFFECTED SOURCE SHEET

| Fugitive Dust Control System Data | Fugitive Dust Control Method 1 |  |
| --- | --- | --- |
|  | Design Water Flow Rate (gpm) 2 |  |
|  | Chemical Additive 3 |  |
|  | Water/Additive Mix Ratio 4 |  |
|  | Amount (gal/yd) 5 |  |
|  | Frequency of Application 6 |  |
|  | Haulroad Surface 7 |  |
|  | Work/Storage Area Surface 8 |  |
|  | Haulroad Length 9 |  |
|  | Number of Vehicles per day 10 |  |
|  | Number of Wheels per Vehicle 11 |  |
|  | Weight of Vehicle (tons) 12 |  |

1.Enter the fugitive dust control method(s) using the following codes:

WT  Water Truck                            WS  Fixed Water Sprays

UW  Underbody Truck Wash          RS  Rumble Strips

OT  Other  ___________________________   (please specify)

2. Enter the design water flow rate for the water truck or fixed water sprays in gallons per minute.

3. Enter manufacturer and type, specification or grade of chemical additive.

4. Enter the water/chemical additive mix ratio.

5. Enter the amount of water or water/chemical additive mix to be applied to haulroads, storage and work areas in gallons per square yard.

6. Enter the frequency of application of water/chemical additive mix to haulroads, storage and work areas during periods of dry weather.

7. Enter the type of haulroad, work and storage area surface (asphalt pavement, concrete, dirt, coarse gravel, reddog, etc.).

8. Enter the approximate length of haulroad(s) in miles or feet. List appropriate units.

9. Enter the maximum daily vehicle traffic (trucks per day).

10. Enter the maximum number of wheels per vehicle.

11. Enter the mean vehicle weight in tons.

12. Complete a separate HMA Plant Fugitive Dust Control System Data sheet for each fugitive dust control system.

Provide a written description of the concrete batch plant’s particulate matter capture system below:

CBP STORAGE TANK AFFECTED SOURCE SHEET

| Source Identification Number1 | Content2 | Length3 (ft) | Dia4 (ft) | Volume5 (gallons) | Throughput6 (gal/yr) | Orientation7 | Liquid Height8 (ft) |
| --- | --- | --- | --- | --- | --- | --- | --- |

1.Enter the appropriate Source Identification Number for each storage tank located at the concrete batch plant.

Storage tanks should be designated T-1, T-2, T-3, etc.

2.Enter storage tank content (#2 fuel oil, asphaltic cement, water, etc.)

3.Enter storage tank length in feet.

4.Enter storage tank diameter in feet.

5. Enter storage tank volume in gallons. Storage tank volume may be calculated using the following mathematical relationship:

(length of tank) X (area conversion) X (tank diameter)2 X (liquid volume conversion) or,

(Ltank  ft) X (3.14/4) X (d2tank  ft2) X (7.48 gallons/ft3)

6. Enter storage tank throughput in gallons per year.

7. Enter storage tank orientation using the following codes:

VERT  Vertical Tank            HORZ  Horizontal Tank

8. Enter storage tank average liquid height in feet.

9. Storage tank emissions may be calculated using TANKS emission calculation program.

CBP EMISSION SUMMARY SHEET

| Source | PM | PM10 |
| --- | --- | --- |
|  | PTE (lb/hr) | PTE (ton/yr) | PTE (lb/hr) | PTE (ton/yr) |
| Total Aggregate Transfer Emissions1 |  |  |  |  |
| Total Sand Transfer Emissions1 |  |  |  |  |
| Cement Unloading to Elevated Storage Silo (Pneumatic)2 |  |  |  |  |
| Pneumatic Cement Additive Unloading to Silo2 |  |  |  |  |
| Weigh Hopper Loading3 |  |  |  |  |
| Mixer Loading (Central)3 |  |  |  |  |
| Truck Mix Loading3 |  |  |  |  |
| Paved Haulroads4 |  |  |  |  |
| Unpaved Haulroads4 |  |  |  |  |
| Wind Erosion from Storage Piles5 |  |  |  |  |
| Total |  |  |  |  |

1. Enter the potential to emit of PM and PM10 associated with the transfer of sand and aggregrate from stockpiles to elevated bins. Use appropriate emission factors and/or equations from the CBP Emission Factor Sheet. Emission calculations may also be determined using spreadsheet G50ECALC.

2. Enter the potential to emit of PM and PM10 associated with the pneumatic transfer of cement and cement additive to storage structures or silos. Use appropriate emission factors and/or equations from the CBP Emission Factor Sheet. Emission calculations may also be determined using spreadsheet G50ECALC.

3. Enter the potential to emit of PM and PM10 associated with loading of weigh hopper(s), central mixer and trucks. Use appropriate emission factors and/or equations from the CBP Emission Factor Sheet. Emission calculations may also be determined using spreadsheet G50ECALC.

4. Enter the potential to emit of PM and PM10 associated with vehicle activity on paved or unpaved haulroad(s). Use appropriate emission factors and/or equations from the CBP Emission Factor Sheet. Emission calculations may also be determined using spreadsheet G50ECALC.

5. Enter the potential to emit of PM and PM10 associated with wind erosion from sand and aggregate stockpiles. Use appropriate emission factors and/or equations from the CBP Emission Factor Sheet. Emission calculations may also be determined using spreadsheet G50ECALC.

6. Attach all potential emission calculations/spreadsheet output to this CBP Emission Summary Sheet.

General Permit Levels

Construction, Modification, Relocation, Administrative Update

Class II General Permits – G10-C (Coal Preparation and Handling), G20-B (Hot Mix Asphalt), G30-B (Natural Gas Compressor Stations), G35-A (Natural Gas Compressor Stations with Flares/Glycol Dehydration Units), G40-B (Nonmetallic Minerals Processing), G50-B (Concrete Batch Plant), G60-B (Emergency Generators)

Class I General Permit - G65-B (Emergency Generators)

| General Permit | Public Notice | Review Period as per 45CSR13 | Application Fee | Criteria | Application Type |
| --- | --- | --- | --- | --- | --- |
| Class II General Permit (Construction ) | 30 days (applicant) | 90 days | $500 + applicable NSPS fees | 6 lb/hr and 10 tpy of any regulated air pollutant OR 144 lb/day of any regulated air pollutant, OR 2 lb/hr of any hazardous air pollutant OR 5 tpy of aggregated HAP OR 45CSR27 TAP (10% increase if above BAT triggers or increase to BAT triggers) or subject to applicable standard or rule, but subject to specific eligibility requirements | Registration Application |
| Class II General Permit (Modification) | 30 days (applicant) | 90 days | $500 + applicable NSPS fees | Same as Class II General Permit (Construction) but subject to specific eligibility requirements | Registration Application |
| Administrative Update (Class I) | None | 60 days | None | Decrease in emissions or permanent removal of equipment OR more stringent requirements or change in MRR that is equivalent or superior | Registration Application or Written Request |
| Administrative Update (Class II) | 30 days (applicant) | 60 days | $300 + applicable NSPS fees | No change in emissions or an increase less than Class II Modification levels | Registration Application |
| Relocation | 30 days (applicant) | 45 days | $500 + applicable NSPS fees | No emissions increase or change in facility design or equipment | Registration Application |
| Class I General Permit | None | 45 days | $250 | Same as Class II General Permit (Construction) but subject to specific eligibility requirements | Registration Application |